## Slide 1: OSG Area Coordinators
Network Monitoring Update: February 18, 2015
Shawn McKee

## Slide 2: Key Initiatives in Network Area
Improving perfSONAR-PS toolkit for OSG
  Numerous small issues found with 3.4.1: excessive logging, services not always cleaning up correctly, missing info in host JSON.
  perfSONAR 3.4.2RC out by the end of this week
OSG modular dashboard service / OSG network service
  MaDDash (metrics GUI) and OMD (service checks) on OSG VM.
    OMD (pfomd.grid.iu.edu) effectively in production
  “Datastore” in pilot state. RSV probes to load DB problematic…
  Mesh-creation automation working, effectively in production.
Documentation updates: network tools & troubleshooting
  Minor wording and instruction updates to address issues found.
Outreach and community interaction
  Participated in LHCONE/LHCOPN meeting. Presented on perfSONAR at Cambridge last week
  Co-chaired WLCG Network and Transfer Metrics WG (last today)
  Ongoing meetings/interactions with perfSONAR developers
  PuNDIT (OSG satellite) working with perfSONAR testbed in OSG

## Slide 3: Recent Accomplishments
Worked with OSG Operations (Soichi) on OSG Network Services
  Updates on OMD monitoring and tests. Much easier to identify issues now.
  Improved configuration on (re)deployment of the OSG OMD instance
  Have a new “Esmond freshness” test identifying missing test results vs expected
Completed update campaign. All but 2 of 221 perfSONAR instances are upgraded to 3.4.1(http://grid-monitoring.cern.ch/perfsonar_coverage.txt)
Updated documentation installed in OSG
  Feedback based upon users experiences has clarified/improved our instructions
  Policy issues under discussion but we have “drafts” in place (IPv6 and Tier-3 items)
  ATLAS (and other LHC VOs) interested in using perfSONAR to test IPv6
Lots of work with the WLCG community.
  Advertised OSG mesh-configuration services broadly. Very well received
  Today presented a tutorial/overview on the perfSONAR Esmond datastore hosted by OSG (See https://indico.cern.ch/event/372546/ )
  Scale of WLCG deployment may be exposing “rare” bugs with perfSONAR
LHCONE point-to-point test-bed previewing “network control”.

## Slide 4: Top Concerns
OSG Network Datastore has been problematic
  Instance had to be shutdown a few weeks ago because of load on OSG’s virtualized infrastructure
  Concerns about chosen architecture for:
    Gathering the data (currently RSV probes)
    Supporting the Esmond database (mismatch in resource type?)
  WLCG and ANSE projects ready to use data ASAP
  Need a path to a production datastore for our network metrics (discussion at end about this)
Reliably gathering perfSONAR metrics (related to datastore above)
  We have developed new tests comparing the data we have versus what we should have. There are gaps
    Sometimes firewall or host-down problems
  We may be finding some subtle bugs in perfSONAR
    Dual-stack hosts IPv6/IPv4 testing to IPv4 only sometimes missing
    Tests not always completing and therefore “blocking”
    Working with perfSONAR developers to find/fix bugs

## Slide 5: Questions or Comments? (Next: discuss datastore)
Thanks!

## Slide 6: URLs of Relevance
Network Documentation https://www.opensciencegrid.org/bin/view/Documentation/NetworkingInOSG
New Deployment documentation for both OSG and WLCG hosted in OSG (migrated from CERN)
  https://twiki.opensciencegrid.org/bin/view/Documentation/DeployperfSONAR
New 3.4 MA guide https://code.google.com/p/perfsonar-ps/wiki/MeasurementArchiveClientGuide
Modular Dashboard Replacement Prototypes
  http://maddash.aglt2.org/maddash-webui https://maddash.aglt2.org/WLCGperfSONAR/check_mk
perfSONAR-PS Installation Motivation:
  https://twiki.grid.iu.edu/bin/view/Networking/WhyPerfSNOAR
Esmond install info http://antg-dev.es.net/esmond-docs/rpm_install.html
Mesh-config in OSG https://oim.grid.iu.edu/oim/meshconfig