## Slide 1: OSG Area Coordinators
Network Monitoring Update: August 16, 2017
Shawn McKee

## Slide 2: Status of Issues from Last Time
Rebalancing of VM resources successful
  Small tweaks to fix some remaining issues
Successfully migrated mesh-configuration from MyOSG/OIM to the new standalone instance (http://meshconfig.grid.iu.edu)
  URL redirection in place for toolkit instances using the old URL
  Docs updated to point to new location
The ETF monitoring instance has been updated and is working well

## Slide 3: OSG Network Services Status
Since the last meeting the OSG network services have been running well (mostly)
  Some issues with RSV stopping mysteriously
  Edgar couldn’t find a root cause
  Restart of rsv fixes the issue
No significant other issues discovered and services are generally running well
  Would like to maintain current status of ‘non-production’ until RSV issues are resolved and new data flow is in place and tested

## Slide 4: perfSONAR Update Released
Yesterday the perfSONAR developers release perfSONAR v4.0.1
  This is a minor feature and bugfix release.
  Sites with auto-updates enabled will automatically install the release sometime in the next few days
  For a list of changes see https://www.perfsonar.net/release-notes/version-4-0-1/
As of mid-day today about 15% of our instances had upgraded.
  We expect ~80% to be upgraded in about 48 hours

## Slide 5: Updated Documentation
Our existing documentation at https://twiki.opensciencegrid.org/bin/view/Documentation/NetworkingInOSG has been revised
  Streamlined
  Updated for v4.0
The perfSONAR developers provide excellent documentation on installation and configuration of perfSONAR
  We pointed to that and provided details on the few specific things we need to worry about for OSG/WLCG installations
    Firewalls configured allowing our access to the data
    Configuration for auto-mesh and information about MCA
    Information about OSG network services
    Information about OSG and WLCG support
Two reviewers of the docs suggested some updates…

## Slide 6: Documentation Additions Planned
Create a page discussing http and https requirements
  The pscheduler now requires port 443 to be open between perfSONAR instances that test to one another
Add some sections to cover important deployment options
  Deployment models (VMS, containers, etc) and their pros/cons
  Multiple NICs and their pros/cons
  Requirements for bandwidth vs latency perfSONAR boxes
Describe psetf (Experiments Testing Framework for perfSONAR; see https://psetf.grid.iu.edu/etf/check_mk/ )
Update the FAQ for new tests available in perfSONAR v4.x
Augment troubleshooting information to enhance pS troubleshooting web page
Create page on installation/upgrade to CentOS7 so users know they don’t need to migrate their data
Refactor docs to provided a better detailed a step-by-step guide

## Slide 7: Recent GGUS Network Tickets
Contacted by CERN about Pakistan transfer issues
  Transfer rates are ~< 2 Mbps
  perfSONAR results showed problem was some kind of network shaper/limiter
Lancaster – SARA (bad link on a LAG)
Dubna – Moscow (Bad fiber identified)
Transfer to Oxford (dCache issue)
Brazil (CBPF) to elsewhere (MTU issue)

## Slide 8: Action Items from the Retreat
During the retreat we identified a few action items
  We wanted to start gathering the HTCondor Schedd network information
  We wanted to change the network data pipeline to ensure the critical services for OSG networking were within OSG control
  We will decrease our reliance on Esmond, keeping the current instance for only a few weeks of data (supports MaDDash)

## Slide 9: Current Net Metrics Flow
perfSONAR RSV
(gathers net metrics)
ESmond Measurement Archive
perfSONAR
Toolkits
CERN Message Bus
(stomp protocol)
GOC Message Bus
(RabbitMQ protocol)
MaDDash
(+data access)
UC ElasticSearch
(for analytics)
FNAL
(data to tape)
Data Cleaning

## Slide 10: Planned Pipeline Changes
The data pipeline will be modified to have use the GOC RabbitMQ message bus.
  Raw JSON data will go to tape at FNAL for long term storage
  Network metrics will be sent to ElasticSearch at Nebraska for use in non-interactive exploration and display of data, e.g., 1 year graphs of quantities of interested updated daily
  Network metrics currently be read from CERN’s bus and sent to UC will be reconfigured to use the OSG message bus as a source
    Data cleaning and transformation is currently done by Ilija using a VM at CERN. This will be migrated to the US and will use the GOC bus
    The STOMP protocol will be enabled on the GOC bus
  We will continue to send data to CERN for their use
  We will reconfigure ESmond on OSG to only host a few weeks of data to support our MaDDash instance (to quickly view net status)

## Slide 11: Planned Net Metrics Flow
perfSONAR RSV
(gathers net metrics)
ESmond Measurement Archive (1 month)
perfSONAR
Toolkits
CERN Message Bus
(stomp protocol)
GOC Message Bus
(RabbitMQ protocol)
MaDDash
(+data access)
UC ES
(analytics)
NL ES
(diagram)
FNAL
(tape)
CERN clients
Data Cleaning

## Slide 12: Results of Changes
While it may some more complex, the pipeline changes result in simplifications in use and operations
  All critical data stays within OSG controlled resources allowing easier debugging and management
  One primary bus setup at GOC that we need to worry about
  Data endpoints have very specific tasks allowing simpler configuration and better resource use
  The Esmond instance can be very much scaled down. No need to address data lifecycle management via Esmond!
Enables a future improvement: perfSONAR 4.1 should support central configuration to send data from our toolkit instances directly to a RabbitMQ bus like the one at GOC

## Slide 13: Status of Retreat Changes
Lincoln Bryant / UC tried to reconfigure HTCondor per instructions to cause it to emit the network data to a log file.
  Didn’t work: “I tried turning on the recommended knobs but never saw any network logging.”
Data pipeline reconfiguration has not happened yet…Ilija, Shawn and others too busy with various meetings since the retreat
Esmond use in OSG still working OK. Next steps will be to setup 8 week limit on the data retained.

## Slide 14: New ‘https’ issue found
Since the release of perfSONAR 4.0 we have seen issues in measurement coverage (enabled by our new dashboards)
  We have identified an issue: perfSONAR 4.0 now requires port 443 (https) be open between instances.
    We previously told sites to open either 80 or 443
  A test from site ‘A’ to site ‘B’ initiated by site ‘B’ requires that site ‘A’ upload its results to site ‘B’ via https (pscheduler) and some sites block 443
  We will discuss this at the next perfSONAR developers meeting tomorrow

## Slide 15: Publishing New Dashboards?
We (Marian Babik and I) are almost ready to publish some new Kibana dashboards which provide useful task-specific information for various use-cases:
  Site problems
  Link problems
  perfSONAR infrastructure problems
  R&E network visibility
Question to OSG: are we ready to do this?
  Concern is that the UC analytics platform really needs to be “production” level once we point users at these new dashboards
  Discussion? Additional concerns? Suggestions?

## Slide 16: Involving an Undergraduate in OSG Networking
I am putting together an UROP proposal (Undergraduate Research Opportunity Program) to have an suitable undergraduate work with me on OSG network related tasks
  Would be for Fall 2017 (no cost to OSG)
  If they work out I can offer to hire them hourly continuing forward
  Proposal is due August 21st

## Slide 17: Concerns
Issue with https needs resolving: what should we tell our sites?
Need to implement data pipeline changes but will require help from outside OSG networking
  Main issues are location of VM for data cleaning/augmentation and setup of GOC message bus to support “transparent” change for VM to receive data
Still on the list: recruit additional non-WLCG sites using our developing capabilities as a “carrot” (new dashboards and docs will help)

## Slide 18: Questions or Comments?
Thanks!

## Slide 19: URLs for Reference
OSG Network Datastore Documents
  Operations https://docs.google.com/document/d/1l144BSo-88M0cLMMjKcKMIE-Q5s21X-w3lYl-0Pn_08/edit#
  SLA https://twiki.grid.iu.edu/bin/view/Operations/PSServiceLevelAgreement
  Data lifecycle https://docs.google.com/document/d/1mJ1kf43nZf6gvKoNtiTOc0g0MYDv_wSfSm7YdiMs3Lo/edit#
Current OSG network documentation https://www.opensciencegrid.org/bin/view/Documentation/NetworkingInOSG
OSG networking year-5 goals and milestones: https://docs.google.com/document/d/1FzmXZinO4Pb8NAfd5SWUzaAFYOL23dt66hQsDmaP-WI/edit
perfSONAR adoption tracking: http://grid-monitoring.cern.ch/perfsonar_coverage.txt
Deployment documentation for both OSG and WLCG hosted in OSG (migrated from CERN)
  https://twiki.opensciencegrid.org/bin/view/Documentation/DeployperfSONAR
ATLAS Analytics:
  Packet-loss: http://tiny.cc/PktLossNoUnknown (6 month view)
  perfSONAR dashboard: http://tiny.cc/pSDash
  perfSONAR link details: http://tiny.cc/pSLink
Mesh-config in OSG https://meshconfig.grid.iu.edu/
Pre-Production Meshconfig https://meshconfig-itb.grid.iu.edu/
perfSONAR homepage: http://www.perfsonar.net/