## Slide 1: OSG Area Coordinators
Network Monitoring Update: May 7, 2014
Shawn McKee

## Slide 2: Key Initiatives in Network Area
OSG modular dashboard service / OSG network service
  The prototype monitoring is ready to migrate to OSG
  Need “Datastore” component one way or another
Improving perfSONAR-PS toolkit for OSG
  Release 3.3.2 available on February 3. Fixed all known issues except intermittent PingER DNS lookup issue (PingER will be removed)
  New version 3.4 in the works (lots of good updates)
  Still need to get ALL OSG sites to install
Documentation updates: network tools & troubleshooting
  No major updates since internal review
  Working on some How-to Debug examples for MaDDash
    See WLCG presentation https://indico.cern.ch/event/289680/
Outreach and community interaction
  Attended LHCONE/LHCOPN last week(see URL above)
  Planning new “Networking and Transfer Metrics WG” in WLCG

## Slide 3: Top Concerns
Prototyped dashboard/monitoring replacement working but now needs to migrate into OSG
OSG Network Service into “production” and fully functional
  Need a way to store the data. Options:
    Leverage upcoming perfSONAR MA in version 3.4. Info at https://code.google.com/p/perfsonar-ps/wiki/MeasurementArchiveClientGuide (timescale ~few months?)
    Build our own? Soichi exploring MongoDB
    Use old version (not really viable)
      Misses traceroute and pinger data.
      Based upon orphaned dashboard code
  Replacement needs to be evolved
    Need OSG “home” to migrate prototype replacements into.
  We should start migrating/consolidating into OSG Operations
Automate creation of the mesh-config from OIM/GOCDB
  Discussed with Soichi
    Need more meta-data (which sites are in which clouds, emails, names, lat./long.)
  Have all sites register in OIM instead of GOCDB/OIM?
Breadth of deployment: We have only WLCG-OSG sites with deployments.

## Slide 4: Recent Accomplishments
Finished WLCG perfSONAR deployment task-force
  Final report at https://indico.cern.ch/event/309125/
  All but 8 sites deployed in WLCG and 6 of those working on it
Planning with Rob/Soichi on OSG networking service
Continued testing/maintenance on alternative components for the Modular Dashboard
  See http://maddash.aglt2.org/maddash-webui for MaDDash implementation
  See https://maddash.aglt2.org/WLCGperfSONAR/check_mk for OMD (login is WLCGps and pw given on call)
  ESnet is very supportive. MaDDash will be supported for foreseeable future
Engagement with LHCONE/LHCOPN, WLCG and GDB communities at recent meetings at CERN, Rome
  Positive feedback.
  Strong interest in being able to ACCESS the network metrics
  Need to get the data gathered and accessible for “clients”
  Planning new WLCG working group to ensure metrics are being regularly collected and available. Needs discussion….

## Slide 5: Soichi’s notes on recent discussion: Tasks on Soichi’s list for 2014…
Host OMD (Open Monitoring Distribution) and MaDDash instances at GOC. Shawn currently runs his OMD and MaDDash instances on his VMs. We need to host these services at GOC after creating install scripts for them. OMD and MaDDash can run on the single VM instance.
  Following are Shawn's current instances
  MaDDash (see http://maddash.aglt2.org/maddash-webui/index.cgi?dashboard=WLCG%20sites ) to provide the test overview
  OMD (http://omdistro.org/start ) to check end-host services (see https://maddash.aglt2.org/WLCGperfSONAR/check_mk/index.py?start_url=%2FWLCGperfSONAR%2Fcheck_mk%2Fview.py%3Fview_name%3Dhostgroups ) [credentials WLCGps/xxxx]
Replace our existing perfsonar.grid.iu.edu (which runs MaDDash-collector and TomW's datastore v2) with services from item #1 and update MyOSG to use MaDDash -MaDDash can consume mesh configs just like Tom's datastore could, and I believe it already allows JSON export of various data.
#3(a) Update OIM/Perfsonar service entries to include all necessary parameters in order to generate a valid mesh config. Shawn will look into a possibility for WLCG to register their perfsonar instances on OIM so that we can generate mesh config for both OSG and WLCG sites.
#3(b) Update OIM/SE services to include list of *nearest* perfsonar instances to be used for each SE. This allows programmatic querying of perfsonar instance from the SE URL.
#4 Continue R&D on collecting information on MongoDB & aggregate information for specific end-user use-cases - similar to how GOC rsvprocess aggregates information from RSV-Gratia DB in order to generate status graphs for MyOSG.

## Slide 6: OSG Network Service Datastore
To me this is the “biggest” issue
We can collect perfSONAR data now
  Current OSG service gets data via SOAP
    Slow, lots of overhead
    Getting data for USCMS and USATLAS sites into OSG
But…No place to keep it?
  Old datastore (orphaned code) missing traceroute
  We need to have a way to store:
    Traceroute (taken 1/hour between all sites)
      Kept for 45 days or longer
    Latency/packet-loss (continuous)
      Save results each minute? Keep for 45 days?
    Bandwidth (1/6-hours within clouds, 1/week WLCG-wide)
      Keep for 3 months?
New MA coming which *may* work…

## Slide 7: perfSONAR v3.4 Measurement Archive (MA)
New measurement archive being developed with a RESTful interface
  At least 100 times faster to query
  Extensible for including new metrics
  Still a few months away (June 2014)
  Timeline https://code.google.com/p/perfsonar-ps/wiki/RoadMap
  Open for comments/input now
Will this work for us? Can we wait?
Perl API http://code.google.com/p/perfsonar-ps/wiki/MeasurementArchivePerlAPI

## Slide 8: Near term items
Test/Explore v3.4 MA…will this work as OSG datastore?
Migrate prototypes into OSG…
  Goal is one service/dashboard for OSG (and WLCG)
  Lots of questions about integration with MyOSG vs standalone components
  Define Operations responsibilities vs OSG/WLCG’s
Expand automated creation of “mesh-configs”
  Prototype and test creation of WLCG meshes.
  Needs interaction between Soichi and CERN/GOCDB experts.
Continue upgrades for sites with perfSONAR-PS versions prior to 3.3.2 (33 sites); ensure mesh-config use
  Identify and lobby non WLCG OSG sites to install
Using and improving the OSG network service
  As sites upgrade and use the mesh, verify data, displays
  Begin testing “clients” of OSG network metrics
    Will require some API changes to get certain typical queries
Continued documentation updates and additions
  Maintain/update documented procedures

## Slide 9: URLs of Relevance
Network Documentation https://www.opensciencegrid.org/bin/view/Documentation/NetworkingInOSG
perfSONAR-PS OSG Installation Instructions
  https://twiki.opensciencegrid.org/bin/view/Documentation/PerfSONARToolKit
New 3.4 MA guide https://code.google.com/p/perfsonar-ps/wiki/MeasurementArchiveClientGuide
Modular Dashboard Replacement Prototypes
  http://maddash.aglt2.org/maddash-webui https://maddash.aglt2.org/WLCGperfSONAR/check_mk
perfSONAR-PS Installation Motivation:
  https://twiki.grid.iu.edu/bin/view/Networking/WhyPerfSNOAR
Initial OSG mesh details http://confluence.grid.iu.edu/display/CENTRAL/Perfsonar+Mesh+Configs

## Slide 10: Questions or Comments?
Thanks!