## Slide 1: OSG Area Coordinators
Network Monitoring Update: April 22, 2015
Shawn McKee

## Slide 2: Key Initiatives in Network Area
Improving perfSONAR-PS toolkit for OSG
  perfSONAR 3.4.2 widely deployed (180 out of 233 on 3.4.2)
  Track details at http://grid-monitoring.cern.ch/perfsonar_coverage.txt
OSG modular dashboard service / OSG network service
  “Datastore” in pilot state. Debugging RSV probes/datastore
Documentation updates: network tools & troubleshooting
  Clarified install details. Updated OSG command line tools page
Outreach and community interaction
  Participated in WLCG and CHEP meetings. Presented on perfSONAR at both meetings last week.
  Co-chairing WLCG Network and Transfer Metrics WG
    Last meeting April 8 next meeting May 6
  Ongoing meetings/interactions with perfSONAR developers
  PuNDIT (OSG satellite) working with perfSONAR testbed in OSG. Testing Pythia (problem ID’ing) next week.

## Slide 3: Recent Accomplishments
Version 3.4.2 of perfSONAR out and auto-updated at most sites
  All known issues addressed; some sites still need to clean remnants of excessive logging
Progress on datastore; production datastore hardware defined; getting pricing
Code to publish network metrics to a message bus exists and being tested.
  Proposed as a quick way to help debugging and allow easy access
Numerous issues fixed/addressed for specific instances
  Mis-configured; bad hardware; residual problems from 3.4.1; firewalls
New effort from WLCG to follow-up with problematic perfSONAR instances started this week (6 month qualification task for ATLAS at 0.5 FTE)
Updating of bandwidth and traceroute tests underway
  Tested/debugged new metrics on OSG perfSONAR testbed last 2 weeks
  Switching from Iperf to Iperf3; traceroute to tracepath
  Transition this week; benefit is more information (MTU) and better metrics for BW
New metrics on data-freshness implemented
LHCONE point-to-point test-bed previewing “network control”. Have Caltech, Michigan and Vanderbilt working with circuits via Internet2/Esnet. Adding UTA and Florida.

## Slide 4: Known Issues
MaDDash using the datastore has filter issue (cells are not properly split top/bot)
Esmond issues
  Correct ways to query uncertain
  Load issues being investigated
Some perfSONAR instances “clogged” with remnants from 3.4.1 or before
No easy way to configure meshes for non WLCG sites
Underpowered perfSONAR instances (<4GB ram) having problems in some cases
Some perfSONAR instances not auto-updating or not exposing all needed info.
No way defined (yet) to migrate datastore (Esmond) to new hardware or to archive old data to different locations

## Slide 5: Top Concerns
OSG Network Datastore is primary focus
  Weekly meetings of a subgroup: target production by July
  Plan is in place to get to release
  Definition of hardware complete; awaiting details
  Debugging of coverage and validity ongoing.
    Intermittent BW data multiplication (x2 or x3) still occurring
    Data matching between central datastore and remote has issues
    Possible problems in time intervals in queries being explored…
  Proposal to update RSV pilots to publish to message bus at CERN. Would aid in debugging
  Have an extended group: (Edgar/OSG, Jorge/ANSE, Marian/WLCG, Henryk/WLCG/LHCb) investigating datastore loading, publishing, accessing issues.
Still 41 instances with multiple problems or offline.
  Follow-up started via ATLAS qualification task
No easy way to get non-WLCG sites in meshes.
  Would like to automate finding test-points by site
  Need standalone mesh-config-util to allows sites control

## Slide 6: Questions or Comments?
Thanks!

## Slide 7: URLs of Relevance
Network Documentation https://www.opensciencegrid.org/bin/view/Documentation/NetworkingInOSG
Networking CLI tools: https://twiki.grid.iu.edu/bin/view/Documentation/Release3/NetworkPerformanceToolkit
New Deployment documentation for both OSG and WLCG hosted in OSG (migrated from CERN)
  https://twiki.opensciencegrid.org/bin/view/Documentation/DeployperfSONAR
New 3.4 MA guide https://code.google.com/p/perfsonar-ps/wiki/MeasurementArchiveClientGuide
Modular Dashboard Replacement Prototypes
  http://maddash.aglt2.org/maddash-webui https://maddash.aglt2.org/WLCGperfSONAR/check_mk
perfSONAR-PS Installation Motivation:
  https://twiki.grid.iu.edu/bin/view/Networking/WhyPerfSNOAR
Esmond install info http://antg-dev.es.net/esmond-docs/rpm_install.html
Mesh-config in OSG https://oim.grid.iu.edu/oim/meshconfig
perfSONAR homepage: http://www.perfsonar.net/