## Slide 1: Initial thoughts on an ESnet Performance Working Group OSG Council Meeting, Aug. 2-3
William Johnston
Eli Dart
Energy Sciences Network (ESnet)

## Slide 2: ESnet has a long track-record in working to solve network performance issues for data-intensive science
With the advent large-scale distributed systems as key elements in the way science is conducted, ESnet has played an important role in debugging end-to-end network performance across many network domains.
  ESnet engineers have taken a lead role in defining, developing, and orchestrating the deployment of perfSONAR – the first multi-domain network test and performance monitoring capability
  For identifying and repairing degraded paths, in most cases, a binary search / divide and conquer approach across domains, and then links in a domain, can fairly quickly isolate the source of the degradation
    This sort of debugging is well suited to the current structure and operating practices of ESnet and many other networks – that is, rotating responsibility for on-call coverage by engineers
    This works less well when the problem stretches out to a long period of time and many people end up involved as one rotates out and another rotates in

## Slide 3: ESnet has a long track-record in working to solve network performance issues for data-intensive science
However, as data-intensive science increases its use of the network a somewhat different model is needed.
Background
  ESnet has a small staff for the size of the network (especially now with the 100Gb/s network being built) – about 38 FTE (not counting a few people hired specifically to work on the ANI, 100G network project)
    ~4 in management, administration, and accounting
    ~10 in infrastructure support (e.g. Unix systems, databases, etc.)
    ~10 in operations and deployment
    ~2 in internal tools development
    ~2 in advanced development
    ~10 in network engineering
  Most of the WAN expertise is in the Network Engineering Group
  In all, there are about six people with WAN system tuning expertise and all of these people have full time jobs in their own group

## Slide 4: ESnet has a long track-record in working to solve network performance issues for data-intensive science
Also with the advent large-scale distributed systems, ESnet tends to get involved in end-system issues
  To date, this involvement has mostly been to help people tune systems for high-speed WAN transfers
    this experience is used to build up a knowledge base for self-help service (fasterdata.es.net)

## Slide 5: ESnet has a long track-record in working to solve network performance issues for data-intensive science
  As often as not, once end systems are tuned problems then become apparent in the campus infrastructure between the end-systems and the campus interface to the WAN
    In response to this, ESnet has developed a data-intensive science oriented campus LAN model and LAN switch tuning guide
      The model consists of the Science DMZ -- an architecture that enables better treatment of data-intensive WAN transfers – and the Data Transfer Node (DTN), a dedicated system for wide-are data transfer
      This has been put into the knowledge base
      The model has been communicated in various forums, including the DOE NLCIO meetings

## Slide 6: What might an ESnet Performance Working Group look like and how might it function?
Composition
  PWG would be a matrix organization with perhaps one person as the long-term coordinator
  The matrix staffing would, at least initially, be from the half dozen or so ESnet staff with the relevant expertise

## Slide 7: What might an ESnet Performance Working Group look like and how might it function?
Functions
  Continue the development and dissemination of a best practice knowledge base for the use of networks for science
    This includes networks and systems end-to-end
  Provide problem-solving assistance in the use of networks for science, including the practical application of all the information on fasterdata.es.net
  Provide guidance to middleware developers, science programs, and sites to help them more easily reap the benefits that come from the effective use of networks – and add this to the knowledge base when practical
    This might take the form of participating in code design or design reviews if the ESnet staff involved can make the time commitment

## Slide 8: What might an ESnet Performance Working Group look like and how might it function?
Changes from the current approach
  Assign performance related problems to the PWG rather than to the engineer on call
    The appropriate people can be matrixed into PWG for this problem, and they can track it to final resolution

## Slide 9: What might an ESnet Performance Working Group look like and how might it function?
The PWG could act as an umbrella for people matrixed from outside ESnet
  To get people with specific software skills beyond what ESnet staff already has
  To provide more intense code development assistance than ESnet engineers could commit to
  To provide on-going, hands-on testing and diagnosis of code in the WAN environment by people who understand WAN issues well and in an environment where realistic testing is easily accomplished
  The PWG could also serve as a training mechanism for external people
Such people would mostly have to be funded outside of the current ESnet budget

## Slide 10: Data Intensive Science Partnership
There has been discussion about a “DISP” – a Data Intensive Science Partnership
  The idea would be to build a multi-disciplinary center of excellence that would export knowledge and networking expertise to science collaborations that do not have the funding, scale, or internal sophistication necessary to grow the middleware and networking structures that have emerged within HEP
  However, this idea has been raised with the DOE/SC ASCR (computer science, math, ESnet, and supercomputer facilities) program managers and the response at this time is there is no funding available for such an endeavor

## Slide 11: In summary, some of the ideas that we have been discussing
We are committed to the dissemination of best practices, and are already working on this
We are proposing that performance tickets get assigned to a group of people within ESnet that has performance as its core job function, even though the people in the group are matrixed from other parts of ESnet
We are open to multi-organization models for community support
We are attempting to foster larger programmatic support for Data Intensive Science outside the context of HEP
#2 is especially hard because it involves operational changes in a core activity

## Slide 12: Thank you! Questions? Email: wej@es.net, dart@es.net